## Slide 1: USB 3.0-based Super Speed Data Acquisition Systems
Project Guides:
Dr. Navin Kumar HoD, Dept of ECE, ASEB | Ms. R Srividhya Head, DSAS, DSD, PDMG | Mr. Srinidhi M Engr SF, DSAS, DSD, PDMG | Mr. Om Sai Ayyappa Reddy Sci/Engr-SD, DSAS, DSD, PDMG
Team:
Sathyasri S BL.EN.U4ECE18138 | Shariq Akhtar P.P. BL.EN.U4ECE18140 | Talluri Sayanth Kishore BL.EN.U4ECE18157 | Yash Rajesh Umale BL.EN.U4ECE18182

## Slide 2: Agenda
Introduce the project goals and draw motivation on the requirement for such data acquisition systems
Enlist and explain the sub – objectives of the project with emphasis on hardware implementation
Discuss and draw conclusions from the research and findings of relevant conference papers, and summarise their short – comings
Explain the design and implementation of the project, along with suitable analysis pertaining to bulk and loopback transfers
Propose additional features and discuss the future scope of the project

## Slide 3: Introduction
Space exploration (unmanned/ manual) involve logging data using magnetic tape recorders.
  Limited data gathering and storage capabilities
  Mechanical systems prone to failure
Solid-state technology was found as an alternative for these problems.
  Information stored in binary [7] can only be altered by voltage changes in transistors
  Highly reliable, durable and compact.
  Availability of multiple interfaces for telecommand and telemetry.

## Slide 4: Introduction (Contd.)
Solid state recorders (SSRs) are developed to [8]
  Store data during imaging or continuous recording, and then retrieve during ground station visibility (playback)
  Monitor during remote sensing and experimental missions
  Store data and health parameters from multiple flight payloads
The project focusses on
  developing a robust end – to – end system to evaluate the flight model of SSRs
  ensuring SuperSpeed data recording and playback with implementation of compression algorithms among other features using a custom board simulator.

## Slide 5: Objective (Phase – I)
Main Objective:
  To build and deploy a system image/ firmware which implements super-speed data transfers between USB, GPIF and SPI interfaces using the 2 – bit Slave FIFO mechanism, and to verify bulk – IN and loopback transfers across an external master (FPGA or ASIC).

## Slide 6: Objective (Phase – I)
Sub Objectives:
  Configuration of the GPIF state machine and I/O matrix.
  Provide DMA transfer of data for record and playback within the FX3.
  Testing the GPIF state machine with timing diagrams, streamer module and USB Control Utility.
  Testing Bulk-IN data transfers via the FX3 to the FPGA or USB host.
  Verifying the loopback transfer of data.

## Slide 7: Methodology
The Cypress FX3 SuperSpeed Explorer Kit offers a one-package solution for the integration of all aforementioned interfaces. It supports SuperSpeed data transfers over USB 3.0 to other peripherals (GPIF, SPI, UART) within the kit.
The kit uses the AHB architecture for internal DMA and system data transfers, along with the GPIF and SPI interfaces for our application.
The project focusses on developing a firmware for the FX3 to facilitate data transfer between peripherals. The adjoint FPGA will be programmed to run tests on the SSR over multiple interfaces to gauge its reliability.

## Slide 8: Methodology (Contd.)
The overall proposed architecture for the project is as follows:
  The USB host (2.0 or 3.0, usually a PC) is connected to the FX3 via its USB port.
The options are propagated via lanes from the origin USB endpoint to the destination USB endpoint within the FX3.
USB host is connected to the FX3 on the USB front, the FX3 is further connected to an external processor or the FPGA via the GPIF pins.
The FPGA is further connected to the SSR, which happens to be the DUT (device under test).

## Slide 9: Methodology (Contd.)
General proposed architecture for the project

## Slide 10: Literature Survey
Data rate based performance is used to verify if the design and implementation of USB 3.0 conforms to the protocol standards and system requirements.
This paper presents an elaborate description of various facets through which data rate based performance analysis is achieved for USB 3.0 SuperSpeed Bulk OUT transactions.
Deals with the characterization and statistical variation of causative factors for different scenarios to obtain minimum, maximum and ideal data rate thus leading to optimum performance.
Challenges faced include synchronization issues or wrong identification, resulting in misleading results.
[1] C. K. Adithya Rangan, K. Aravinda Holla, V. Kulkarni, A. Kumar and A. Patil, "Data Rate Based Performance Analysis and Optimization of Bulk OUT Transactions in USB 3.0 SuperSpeed Protocol," 2018 Second International Conference on Advances in Electronics, Computers and Communications (ICAECC)

## Slide 11
Presents the design and implementation of a versatile high speed data acquisition system for GNSS signals capable of transferring large amounts of data to a PC.
Global Navigation Satellite System (GNSS): a constellation of satellites providing signals from space that transmit positioning and timing data to GNSS receivers.
Implemented on a Xilinx Virtex UltraScale+ FPGA with a high-throughput data path through the on-board DDR4 SDRAMs, based on which a ring buffer is designed to provide a 2 GB buffering capacity.
In addition, a simple differencing algorithm with threshold detection is integrated into the back end for dynamic frame rate operation.
Literature Survey
[2] J. G. V. Leañez et al., "High-Speed Data Acquisition System for GNSS Applications," 2020 Argentine Conference on Electronics (CAE), 2020

## Slide 12
Emphasis on a system using an FPGA as the core control chip, due to which the FX3 realizes high speed data transmission of the USB 3.0 synchronous Slave FIFO mode through the GPIF pins.
The FX3 SDK is built and shipped along with the microcontroller to ease the design and development of the firmware.
The GPIF II Designer, Eclipse IDE, ThreadX RTOS, USB Control Manager and other design tools are third-party software wrapped in Cypress APIs to enable native integration with the hardware.
A USB device can implement one or more functions, and the capabilities of the device are reported to the host through a set of data blocks called descriptors.
Literature Survey
[3] Tian, Fenxian et al. “Design and Implementation of USB3.0 Data Transmission System based on FPGA.” 3rd International Conference on Computer Engineering, Information Science & Application Technology, 2019

## Slide 13
Investigates building a framework for a test bench that is inexpensive, scalable, open source, and easily implemented.
Reviews modern protocols to rely on USB to provide the physical link and data protocol to interface an FPGA to a PC.
Each state is programmed to perform certain actions, and the conditions are checked on each GPIF II clock edge.
The FX3 device has an internal DMA fabric that connects the GPIF interface to the internal system memory.
Literature Survey
[4] Y. J. Qian and K. Cui, "Design of high speed CCD data acquisition system based on FPGA and USB3.0," 2015 International Conference on Information and Communication Technology Convergence (ICTC)

## Slide 14
  Explores the problem of designing an effective master-slave operating system architecture for multiprocessors.
  Identifies and addresses design issues that have significant impact on the functionality and performance of the master-slave approach.
  Investigates three major issues that are closely related to the architecture and performance of the master-slave approach:
    structural design of a master-slave system
    functional design of remote invocation mechanism
    inherent architectural problem of the master-slave approach
Literature Survey
[5] Minyeol Seo et al. “An Effective Design of Master-Slave Operating System Architecture for Multiprocessor Embedded Systems,” Advances in Computer Systems Architecture, 12th Asia-Pacific Conference, ACSAC, 2007

## Slide 15
FPGAs play a very important role in sensor data acquisition and processing with its rich interface resources and excellent parallel processing ability.
Color image processing by a traditional PC cannot achieve the maximum video display frame rate due to high speed real-time requirements.
Observations show that the FPGA-based video pipeline processing and DDR3 frame cache application can increase the video frame rate and improve the transmission stability of video data.
Literature Survey
[6] Y. Gong and F. Yu, "Design of high-speed real-time sensor image processing based on FPGA and DDR3," 2017 3rd IEEE International Conference on Computer and Communications (ICCC)

## Slide 16: Summarising the papers
Literature Survey
Ref. No. | Observations | Problems
[1] | Description of various facets through which data rate based performance analysis is achieved for USB 3.0 SuperSpeed Bulk OUT transactions. | Synchronization issues or wrong identification, resulting in misleading results.
[2] | A versatile high speed data acquisition system for GNSS signals capable of transferring large amounts of data to a PC was designed. | Absence of a 1553 Bus Controller, relying solely on orthogonally polarized antennas with polarization deficiencies.
[3] | Obtained a system capable of interfacing an FPGA with a host PC using SuperSpeed (USB 3.0) | The design part of the DDR3 controller and the USB3.0 interface in this system are the key points of difficulty.

## Slide 17: Summarising the papers
Literature Survey
Ref. No. | Observations | Problems
[4] | Built a framework for a test bench that is inexpensive, scalable, open source, and easily implemented. | The design goal of 3.2 Gbit/s is restricted by Slave FIFO mode (32 bit,100MHz max clock frequency).
[5] | Identifies and addresses design issues that have significant impact on the functionality and performance of the master-slave approach. | Tasks involving a significant portion of kernel mode operations can make the master a critical bottleneck; especially with multiprocessors.
[3] | Increased video frame rate and improved transmission stability of video data with FPGAs. | Incessant writing and reading can cause pointers to turn around and overlap, resulting in the loss of writing data or the invalidation of reading data.

## Slide 18: Design and Analysis
Configuring the GPIF – II I/O Matrix
  The GPIF II Designer is used for designing the IO matrix, which is responsible for assigning the mapping of pins as per the slave FIFO interface requirements.
A state machine is designed using the tool in order to define the sequence of commands and execution, while ensuring conditional state transitions based on signals from an external processor.
Slave FIFO for transactions between the FX3 and an external master

## Slide 19: Configuring the I/O Matrix
The interface definition window and I/O matrix helps define the electrical interface in terms of:
  data and address buses
  the number and direction of control signals
  the interface clocking parameters
Design and Analysis

## Slide 20: Configuring the I/O Matrix
The I/O matrix helps in configuring
FX3 peripherals such as I2C, UART, SPI
Data bus width
Endianness
Flags to indicate the status of the thread in terms of current buffer conditions
Pin mappings as per the desired interface
Design and Analysis

## Slide 21: Programming the GPIF II State Machine
The GPIF II port provides a parallel interface with maximum of 32 bidirectional data lines. They can be time multiplexed into address lines.
The GPIF II Designer allows the user to
  Create an I/O matrix for mapping pins to signals
  Defining state machines for specific interfaces
  Generate a C header file encoding all of the GPIF definitions
The header file can be used to integrate the GPIF functionality into the slave FIFO application firmware.
Design and Analysis

## Slide 22
Logic Diagram for Synchronous Slave FIFO:
In order to configure the GPIF II interface, the following initial states need to be defined:
Interface type: Slave
Communication type: Synchronous
Endianness: Little Endian
Data bus width: 8 bit, 16 bit or 32 bit
Address or data bus multiplexed
2 address pins for selecting among 4 available threads
Active low signals for Read, Write, Chip Select and Output Enable.
Design and Analysis

## Slide 23: Implementation Logic
The project consists of an FX3 Development Kit interconnected with an evaluation kit (FPGA) using a Samtec to FMC interconnect board.
The interconnect board mates with the Samtec connector on the FX3 and the FMC connector on the FPGA.
For execution and testing of the slave FIFO interface, the following components are included in the firmware.
Design and Analysis

## Slide 24: Implementation Logic
Streaming (IN) data transfer The FPGA does one-directional transfers: continuously writes data to FX3 over synchronous slave FIFO. | Streaming (OUT) data transfer The FPGA does one-directional transfers: continuously reads data from FX3 over synchronous slave FIFO.
Design and Analysis

## Slide 25: FX3 Firmware Application Structure
All FX3 firmware applications consist of two parts:
  • Initialization code – Usually common for all applications
  • Application code – Code specific to the Slave FIFO application
The typical file structure for the firmware application would be as follows:
  A header file containing the GPIF II descriptors for 16-bit and 32-bit slave FIFO interface
  A C program containing USB descriptors
  A header file containing defines used in the main application. Several important constants essential for setting the initial conditions for execution are defined in this file.
  A C program containing the main application logic for synchronous Slave FIFO.
Design and Analysis

## Slide 26
Initialization Code
As part of the device initialization:
The CPU clock is setup.
Vectored Interrupt Controller (VIC) is initialized.
Device caches are enabled (8 kB data cache and 8 kB instruction cache)
I/O’s are configured based on the header files included.
The inherent ThreadX RTOS is invoked, and the OS timer is initialized before transferring the control over to the RTOS scheduler.
Design and Analysis

## Slide 27
Application Code
The Slave FIFO application code comprises of three parts:
The application thread function to perform application – specific initialization operations.
The application start function to set up endpoints and DMA channels required for USB – GPIF data transfers.
The application stop function to free up DMA channels and disable USB endpoints when a USB reset or disconnect is detected.
Design and Analysis

## Slide 28: Application Thread
Initializing the debug mechanism The debug module uses the UART to output debug messages. The UART needs to be configured before the debug mechanism is initialized. needs to be initialized with the requisite parameters. has the transfer size set to infinite The debug module is hence initialized, with two main parameters: the destination for the debug prints (UART socket) and the verbosity of the bug. | Initializing the main slave FIFO application The application initialization consists of the following steps: GPIF II Initialization USB Initialization Initializing the USB stack Registering call-backs Defining USB descriptors
Design and Analysis

## Slide 29: Results and Discussions
USB was chosen as the high-speed data link between the FPGA and PC to leverage the simplicity of a VCP (virtual communication port).
The FX3 SuperSpeed Explorer Kit integrates all of the different operations that interface with the SSR (telemetry, telecommand, etc.) onto a single unit, coupling the advantage of USB 3.0’s high speed data transfer mechanism.
As a precursor to testing solid state recorders, we first implement the Slave FIFO interface to the GPIF pins of the FX3 and configure the microcontroller as explained previously.

## Slide 30: Results and Discussions (Contd.)
To summarize the work and results for phase 1 of the project:
The GPIF II Designer is used to configure the I/O matrix
The state machine for slave FIFO interface is designed and commissioned for integration with the FX3 firmware
Read-write operations are observed with the configured GPIF interface as functions of time and input control signals
A comprehensive firmware application is designed to handle USB/ GPIF callbacks and events, along with DMA configurations, descriptor definitions, thread and process handling along with setting up debug mechanisms.

## Slide 31: Slave FIFO - Read Sequence
The external master drives the two-bit address on the ADDR lines and asserts the read or write strobes.
As observed:
  The FIFO address is stable and SLCS (chip select) is asserted
  SLOE (output enable) is asserted, and it signals the FX3 to drive the data bus.
  SLRD (read) is asserted.
Results and Discussions

## Slide 32: Slave FIFO - Write Sequence
FIFO address is stable and the signal SLCS (chip select) is asserted.
External master/ peripheral outputs the data onto the data bus.
SLWR (write) is asserted.
While SLWR is asserted, data is written to the FIFO. On the rising edge of the clock, the FIFO pointer is incremented.
The FIFO flag is updated after a slight delay from the rising edge of the clock.
Results and Discussions

## Slide 33: Streaming Transfers onto the FX3
The SDK provides a couple of useful tools to track and gauge the extent of data transfer within the microcontroller.
The FX3 firmware application is developed to facilitate data transfer between peripherals.
The USB Control Centre Utility, along with the C++ Streamer tool can be used to quantitatively measure the average throughput observed at the USB and GPIF endpoints.
Results and Discussions

## Slide 34: Observations
* To be added *

## Slide 35: Conclusion and Future Enhancements
The current phase of the project focusses on configuration of the FX3 SuperSpeed Explorer Kit for integration with another external system for performing high speed data transfers and testing solid-state recorders for inclusion in space missions.
It is possible to consider qualified alternatives to the FX3 microcontroller which consist of technological specifications and capabilities far exceeding those of the prescribed SuperSpeed Explorer Kit.
An Nvidia Jetson Nano or a Raspberry Pi 4 may seem like powerful alternatives given their superior CPU and RAM capacity, but they’re not included in the system since they are standalone devices which do not contain extensive SDK support or pin configuration access for implementing interfaces such as slave FIFO on GPIO pins.
The next phase of the project deals with programming an external processor (FPGA) in Verilog. Moreover, the firmware will be combined and shipped within a single package as an image file, subsequently abstracted by a GUI-driven user-friendly application built using Visual Studio and UI/UX tools such as CSS and Bootstrap.

## Slide 36: Conclusion and Future Enhancements
A system image/ firmware built to implement the 2 – bit Slave FIFO mechanism, and to verify bulk – IN and loopback transfers across an external master (FPGA). In order to achieve the above:
The GPIF state machine and I/O matrix were configured
Bulk-IN data transfers via the FX3 to the FPGA and USB host were executed
Loopback transfer of data occurred successfully
A number of faults and challenges including IDE mismanagement, obsolete APIs, timeout errors, streamer and GPIF definition conflicts were encountered.

## Slide 37: Future Enhancements
Task | Tentative Completion
Implementing a 1553 Bus Controller and building software to target the same | January – March 2022
Generating and receiving command packets for 1553 BC, pulse command and simulator FPGA to forward over an SPI interface | February – March 2022
Configuring the FPGA using VHDL to accept commands from the USB host via FX3 and run tests on the SSR | March 2022
Implementing compression and decompression algorithms to handle image and video data from SSR on the fly via FPGA | 

## Slide 38: Future Enhancements (Contd.)
Task | Tentative Completion
Implementing the command receiver to receive and interpret commands over SPI to the FPGA | April 2022
Defining and executing appropriate record/ playback protocols for data retrieval from SSR | February – March 2022
(Optional) – Use FPGA compute resources to perform video analysis and image processing | March 2022
Redesign FX3 firmware and FPGA configurations to facilitate real-time video streaming to FPGA/ from SSR | April – May 2022
Designing an application using Visual Studio to issue telecommand, telemetry and toggle compression for incoming or outgoing data | 

## Slide 39: Project Extension – Phase II
A rough schematic to depict the project extension for phase II.

## Slide 40: References
[1] C. K. A. Rangan, K. A. Holla, V. Kulkarni, A. Kumar and A. Patil, "Data rate based performance analysis and optimization of bulk OUT transactions in USB 3.0 SuperSpeed protocol," 2017 3rd International Conference on Applied and Theoretical Computing and Communication Technology (iCATccT), 2017, pp. 114-119, doi: 10.1109/ICATCCT.2017.8389117.
[2] J. G. V. Leañez et al., "High-Speed Data Acquisition System for GNSS Applications," 2020 Argentine Conference on Electronics (CAE), 2020, pp. 14-19, doi: 10.1109/CAE48787.2020.9046375.
[3] Fenxian Tian, Juan Li, Xinxin Sun and Jun Yang. Design and implementation of USB3.0 Data Transmission System based on FPGA. 3rd International Conference on Computer Engineering, Information Science & Application Technology (ICCIA 2019), Advances in Computer Science Research, 2019.

## Slide 41: References
[4] Y. J. Qian and K. Cui, "Design of high speed CCD data acquisition system based on FPGA and USB3.0," 2015 International Conference on Information and Communication Technology Convergence (ICTC)
[5] Minyeol Seo et al. “An Effective Design of Master-Slave Operating System Architecture for Multiprocessor Embedded Systems,” Advances in Computer Systems Architecture, 12th Asia-Pacific Conference, ACSAC, 2007
[6] Y. Gong and F. Yu, "Design of high-speed real-time sensor image processing based on FPGA and DDR3," 2017 3rd IEEE International Conference on Computer and Communications (ICCC)

## Slide 42: Thank You